3-D Regional Structural Model Construction

Central Baffin Island, Dewar Lakes region, Canada

Authors: Eric de Kemp and Marc St-Onge

Introduction

This 3-D gocad model represents a collection of surface interpretations for a polydeformed thrust fault which cuts the Archean basement-Paleoproterozoic cover rocks in the Central Baffin Island, Dewar Lakes region. It is embedded in the Gocad 2.1.3  project file cbaf_dewar_3d.

The model extends across the greater parts of 1:100,000 GSC Maps OF 4200 and OF 4201, (1:250 000 NTS 37A & 27B) covering approximately 165 km x 120 km (Figure 1), and is dominantly underlain by the 2.0–1.9 Ga Piling Group; poly-deformed mafic to ultramafic metavolcanics, with a spectrum of semi-pelitic to arkosic metasediments and a suite of localized peridotitic and gabbroic intrusions. The reader is referred to reference maps OF 4200 & OF 4201 for colour schemes and bedrock legends depicted in geology terrain drapes of the model as well as marginal notes therein for background geologic information.

Only publicly available map data from Geological Survey of Canada field mapping programs was used in this interpretation.

This study demonstrates the capacity for addressing regionally significant geological problems by conducting targeted high-resolution mapping. Stratigraphic and structural issues such as the delineation of a tectonic versus a stratigraphic boundary can have an impact on the wider regional interpretation. One of the goals of the 3-D component of the 4-D geoscientific study of Central Baffin Island is the construction of regional 3-D bedrock geology models, or what is referred to as  3-D bedrock maps  or “common earth models”. These 3-D interpretive models extend the surface geology upwards and downwards a distance that gives a new dimensionality to the geologic map. In similar fashion to extending 2-D curvilinear map traces by geologic interpretation, complex 3-D curved surfaces are extended beyond the observed erosion surface.

The construction of these 3-D maps is extremely time consuming, and, as with the construction of a 2-D map, is highly interpretive. Enhancing the environment for making these interpretations both in 2-D and in 3-D is the goal of modern geoscience integration. Establishing case studies with associated data sets such as the 3-D data collected in this study is key to developing new tools that optimize the geologic interpretive process.  From this field study high-resolution 3-D field data now exists for this area. By integration of our data with the updated regional stratigraphic model, we will attempt to apply methods to construct a 3-D model which will be reported on at a later date.

Figure 1: Modelled Paleoproterozoic Thrust  fault (Red surface) and Archean Basement-Paleoproterozoic cover contact  (white surface) developed with SPARSE© Using GSC map data. Contour interval on Basement-cover contact 1 km depth.

Database Structure

All data is embedded in a gocad 2.1.3 project file. For data conversion into other formats please see 3'rd party service providers.

Corrections and Additions

Every attempt was made to provide 3-D surface interpretations that are at a minimal constrained to the field observations and associated 2-D map and section interpretations.  Inconsistencies between the various cross-sections and surface maps may appear in this model due to ongoing updating of  the interpretive data sets. Please send feedback or suggestions for a more rigorous updating of the model that will result in a) increased accuracy of the interpreted surfaces, b) more realistic rending of volumes and/or c) better usability for specific exploration and/or communication  activities to Eric de Kemp. Natural Resources Canada, Geological Survey of Canada, 615 Booth Street, Ottawa, ON, Canada  K1A 0E9. Phone (613) 947-3738; Fax: (613) 995-9273; E-mail: edekemp@nrcan.gc.ca.

Acknowledgements

Thanks to Kevin Sprague for providing much needed tools for doing this interpretation with the SPARSE© plug-in to gocad. Thanks also to Mira Geoscience for providing ongoing advice on 3-D integration methodologies used throughout the project.

## Data sources and bibliography

Corrigan, D., Scott, D.J., and St-Onge, M.R.

2001:

Geology of the northern margin of the Trans-Hudson Orogen (Foxe Fold

Belt), central Baffin Island, Nunavut; Geological Survey of Canada, Current Research , no. 2001-C23, 2001; 27 pages.

de Kemp, E.A.

2000a:

3-D visualization of structural field data: Examples from the

Archean Caopatina Formation, Abitibi greenstone belt, Québec, Canada: Computers

and Geosciences, V.26 (2000), pp.509-530.

de Kemp, E.A., Corrigan, D., and St-Onge, M.R.

2001:

Evaluating the potential for three-dimensional structural modelling of the

Archean and Paleoproterozoic rocks of central Baffin Island, Nunavut; Geological Survey of Canada, Current Research , no. 2001-C24, 2001; 22 pages.

Henderson, J.R. and Henderson, M.N.

1994:

Geology of the Dewar Lakes area, central Baffin Island, District of Franklin, N.W.T. (parts of 27B and 37A); Geological Survey of Canada, Open File 2924, scale 1:100 000.

Henderson, J.R., Grocott, J., Henderson, M.N., and Pereault, S.

1989:

Tectonic history of the Lower Proterozoic Foxe-Rinkian Belt in central Baffin Island, N.W.T., in Current Research, Part C, Geological Survey of Canada, Paper 89-1C, p. 186-187.

Henderson, J.R., Grocott, J., Henderson, M.N., Falardeau, F., and Heijke, P.

1988:

Results of field work near Dewar Lakes, Baffin Island, N.W.T., in Current Rsesarch, Part C, Geological Survey of Canada, Paper 88-1C, p. 101(108.

Jackson, G.D.

1978:

McBeth Gneiss Dome and associated Piling Group, central Baffin Island, District of Franklin; in Rubidium-Strontium Isotopic Age Studies, Report 2, (ed.) R.K. Wanless and W.D. Loveridge; Geological Survey of Canada, Paper 77-14, p. 1417.

McGaughey, J.

2002:

Quantitative integration of geology and geophysics through 3D physical

property models, 3-D Modeling for Mineral Exploration and Mining, 1st  annual user group meeting, Sept 24-26 Sudbury, Ontario.

McGaugey, J. and Morrison, K.

2000:

The Common Earth Model: A Revolution in Exploration Data Integration

Annual Meeting of Prospectors and Developers Association, Abstracts, Toronto, Ontario, March, 2000.

Scott, D.J., St-Onge, M.R., and Corrigan, D.

2002:

Geology of the Paleoproterozoic Piling Group and underlying Archean gneiss, central Baffin Island, Nunavut; Geological Survey of Canada, Current Research , no. 2002-C17,10 pages.

2003:

Geology of the Archean Rae Craton and Mary River Group and the Paleoproterozoic Piling Group, central Baffin Island, Nunavut ; Geological Survey of Canada, Current Research , no. 2003-C26; 12 pages.

St-Onge, M.R., Scott, D.J., and Corrigan, D.

2002:

Geology, Straits Bay, Nunavut; Geological Survey of Canada, Open File 4200; 2 sheets.

2002:

Geology, Dewar Lakes, Nunavut; Geological Survey of Canada, Open File 4201; 2 sheets.

Wodicka, N., St-Onge, M.R., Scott, D.J., and Corrigan, D.

2002:

Preliminary report on the U-Pb geochronology of the northern margin of the Trans-Hudson Orogen, central Baffin Island; Radiogenic Age and Isotopic Studies: Report 15; Geological Survey of Canada, Current Research , no. 2002-F7; 12 pages.